## Slide 1: The IEEE 802.16 WirelessMAN™ Standard
http://WirelessMAN.org
Brian G. Kiernan
InterDigital Communications Corp.
Vice Chair, IEEE 802.16 Working Group

## Slide 2: Have you heard ?
IEEE 802.16 is delivering as promised!
Publication (March 2002)
  IEEE Standard 802.16: Air Interface for Fixed Broadband Wireless Access Systems (10-66 GHz)
  Final draft completed and in catalog since October 2001
Publication (10 September 2001)
  IEEE Standard 802.16.2: Recommended Practice- Coexistence of Fixed Broadband Wireless Access Systems (10-66 GHz)

## Slide 3: IEEE 802.16 History
Sponsors
  IEEE Computer Society
  IEEE Microwave Theory and Techniques Society
Project Development: Summer 1998
IEEE 802 Tutorial: November 1998
IEEE Study Group
  November 1998-March 1999
Session #1: July 1999
Session #17: January 2002 Levi, Finland
Session #18: 11-15 March, St.Louis

## Slide 4: IEEE 802.16 by the Numbers
175 Members
39 “Potential Members”
58 Official Observers
>700 different individuals have attended a session
2.8 Million file downloads in year 2000
Members and Potential Members from
  10 countries
  >110 companies

## Slide 5: IEEE 802.16 Project Structure
IEEE Standard 802.16
(published)
MAC
10-66 GHz PHY
Air Interface
(Standard)
P802.16a
2-11 GHz PHY
MAC enhancements
in ballot
Completion: August 2002
IEEE Standard 802.16.2
(published)
10-66 GHz
Coexistence
(Recommended Practice)
P802.16.2a
2-11 GHz
in development
Completion: March 2003

## Slide 6: IEEE P802.16
Standard Air Interface for Fixed Broadband Wireless Access Systems

## Slide 7: P802.16 Scope
Specifies the air interface, including the medium access control layer (MAC) and physical layer (PHY), of fixed point-to-multipoint broadband wireless access systems providing multiple services. The medium access control layer is capable of supporting multiple physical layer specifications optimized for the frequency bands of the application. The standard includes a particular physical layer specification broadly applicable to systems operating between 10 and 66 GHz.

## Slide 8: IEEE P802.16 History
July-Sept., 1999: Functional Requirements
November 1999: 35 Proposals
January 2000: 2 Consolidated Proposals
May 2000: Plan to Merge 2 Proposals
August 2000: Rev. 0
thru February 2001: Working Group Review
February-August 2001: WG Letter Ballot
August-October 2001: IEEE Sponsor Ballot
6 December 2001: RevCom approval
March 2002: Publication

## Slide 9: Point-to-Multipoint Wireless MAN: not a LAN
Base Station (BS) connected to public networks
BS serves Subscriber Stations (SSs)
  BS and SS are stationary
  SS typically serves a building (business or residence)
  provide SS with first-mile access to public networks
Multiple services, with different QoS priority, simultaneously

## Slide 10: PHY Considerations (10-66 GHz)
Broadband Channels
  Wide channels (20, 25, or 28 MHz)
  High capacity – Downlink AND Uplink
Multiple Access
  TDM/TDMA
  High rate burst modems
Adaptive Burst Profiles on Uplink and Downlink
Duplex scheme agnostic
  Time-Division Duplex (TDD)
  Frequency-Division Duplex (FDD) [including Burst FDD]
    Support for Half-Duplex Terminals

## Slide 11: Physical Layer Adaptivity
(burst-by-burst adaptivity not shown)

## Slide 12: Adaptive Burst Profiles
Burst profile
  Modulation and FEC
Dynamically assigned according to link conditions
  Burst by burst, per subscriber station
  Trade-off capacity vs. robustness in real time
Roughly doubled capacity for the same cell area
Known Burst profile for downlink broadcast channel
  All other burst profiles can be configured “on the fly”
  Subscriber station capabilities recognized at registration
Allows innovative schemes to efficiently use the spectrum while remaining interoperable.

## Slide 13: Duplex Scheme Support
On downlink, SS is associated with a specific burst
On uplink, SS is allotted a variable length time slot for their transmissions
Time-Division Duplex (TDD)
  Downlink & Uplink time share the same RF channel
  Dynamic asymmetry
  SS does not transmit & receive simultaneously (low cost)
Frequency-Division Duplex (FDD)
  Downlink & Uplink on separate RF channels
  Static asymmetry
  Half-duplex SSs supported
    SS does not transmit & receive simultaneously (low cost)

## Slide 14: Modulation (10-66 GHz)
Single Carrier QAM, Gray coded
  QPSK
  16QAM
    Mandatory for Downlink, Optional for Uplink
  64QAM
    Optional for both Downlink & Uplink

## Slide 15: FEC
Reed Solomon
  RS GF(256), t = 0…16
For robust communications, the RS code is concatenated with a BCC
  No interleaving, suitable for burst
  BCC is a rate 2/3 block code based on a tail-bite termination of the (7,5)8 Convolutional Code for every 16 data bits
Shortening allowed
Turbo Product Codes (TPC) are optional

## Slide 16: Baud Rates & Channel Size (10-66 GHz)
Flexible plan - equipment manufacturers can choose according to spectrum requirements
QPSK 16-QAM 64-QAM
Channel Symbol Bit Rate Bit Rate Bit Rate
Width Rate
(MHz) (Msym/s) (Mbit/s) (Mbit/s) (Mbit/s)
20 16 32 64 96
25 20 40 80 120
28 22.4 44.8 89.6 134.4

## Slide 17: MAC Requirements
Provide Network Access
Address the Wireless environment
  e.g., very efficient use of spectrum
Broadband services
  Very high bit rates, downlink and uplink
  A range of QoS requirements
  Ethernet, IPv4, IPv6, ATM, ...
Likelihood of terminal being shared
  Base Station may be heavily loaded
Security
Protocol-Independent Engine
  Convergence layers to ATM, IP, Ethernet, ...
Support both TDD and FDD PHY

## Slide 18: 802.16 MAC: Overview
Connection-oriented
Supports difficult user environments
  High bandwidth on demand, hundreds of users per channel
  Continuous and bursty traffic
  Very efficient use of spectrum
Protocol-Independent core (ATM, IP, Ethernet, …)
  ATP-based and Packet-based Convergence layers
Balances between stability of contentionless and efficiency of contention-based operation
Flexible QoS offerings
  CBR, rt-VBR, nrt-VBR, BE, with granularity within classes
Solid privacy and encryption
Many options for vendor innovation and differentiation
  e.g., scheduling
Built for support of multiple PHYs

## Slide 19: Summary
The IEEE 802.16 WirelessMAN Air Interface, addresses worldwide BWA market needs.
The 802.16 MAC is flexible and powerful enough to support any fixed BWA technology variant in any spectrum in any market.
The 802.16 Air Interface provides great opportunities for vendor differentiation, at both the base station and subscriber station, without compromising interoperability.
The outcome was due to successful cooperation between BWA leaders.

## Slide 20: Amendment Project IEEE P802.16a
Media Access Control Modifications and Additional Physical Layers for 2-11 GHz
Covers both Licensed and License Exempt frequency bands

## Slide 21: Key Features of 802.16a Draft PHY (2-11 GHz)
TDD or FDD
  OFDM/OFDMA
  Single-Carrier TDMA
    with optional Frequency-Domain Equalization

## Slide 22: Key 802.16a MAC Enhancements
OFDM Support
ARQ
Mesh Mode
  Optional topology
  License Exempt bands
  Subscriber-to-Subscriber communications

## Slide 23: BWA in ETSI BRAN
HIPERACCESS
  Above 11 GHz
  HIPERACCESS began before 802.16
  Difficulty in resolving processes
  IEEE now well ahead in schedule
HIPERMAN
  Below 11 GHz
  IEEE went first
  Signs of healthy cooperation
  Selected 802.16 MAC and 802.16a OFDM PHY as baseline

## Slide 24: What’s Next ?
Complete 2-11 GHz work
Enhance 10-66 GHz spec
  Interoperability test protocols
    Develop and Publish
    Implement (WiMAX)
Expand reach under 802.16 MAC
Consider support for mobility
Aim to be 4G

## Slide 25
How to Participate
  Attend meetings
    Join us next month in St. Louis
  Read reflector
  Read documents
  Submit documents & comments
  Join sponsor ballot pool!

## Slide 26: Distribution of IEEE 802 Standards

## Slide 27: Conclusions
With its steady progress, IEEE 802.16 is a BWA success story.
The IEEE 802.16 MAC is a future-proof platform supporting an array of services.
The IEEE 802.16 10-66 GHz PHY is coming soon to a chip set near you.
WiMAX will support compliance tests.
IEEE 802.16a (2-11 GHz) this summer.

## Slide 28: IEEE 802.16 Resources
IEEE 802.16 Working Group on Broadband Wireless Access
info, documents, email lists, etc:
http://WirelessMAN.org