## Slide 1: Wireless LANs— Understanding the Options Broadband World Wireless Forum February 13, 2002
David A. Sumi
The Telnecity Group
San Jose, CA
dsumi@telnecity.com
www.telnecity.com

## Slide 2: The Telnecity Group
Strategic Marketing Consulting - Offers a continuum of strategic marketing services to companies in all phases of the company life cycle.
Broadband Intelligence Products - Custom and periodic reports have an initial focus on all wireless markets:
  WLAN (802.11*)
  Fixed Wireless (802.16, satellite, etc.)
  3G/4G
Future Intelligence Products will focus on current and next generation access technologies:
  Cable Modems
  DSL
  PON
  EFM
The Telnecity Group consists of two groups: Strategic Marketing Consulting and Broadband Intelligence Products.

## Slide 3: Agenda
WLAN–Massive opportunity
Standards & Forums
Future Applications

## Slide 4: Chart: WLAN Market
Growth of the market is dependant on current IT spending in the existing strong vertical markets and the expected explosion of the Enterprise market.
$0.0
$0.5
$1.0
$1.5
$2.0
$2.5
$3.0
$3.5
$4.0
$4.5
$5.0
2005
2000
(Billions)
Average
Strategis Unlimited
Frost and Sullivan
In-Stat
IDC

## Slide 5: Market Share of WLAN Access Point Shipments, by Vendor, Worldwide.
Source: InStat, June 2001.
WLAN offers the capability to attract Enterprise and Service Providers under the same roof.
Networking vendors are aggressively pursuing 802.11.
20%
11%
10%
9%
6%
4%
40%
Cisco
Agere
Symbol
Dlink
Enterasys
3Com
Other

## Slide 6: 802.11 First Run
Approved in 1997 after 7 years of development
PHY Layer Review
  Direct Sequence Spread Spectrum & Frequency Hopping Spread Spectrum
  2.4GHz only (2.4GHz-2.4835GHz)
  1 and 2Mbps data rates
  20MHz channels DSSS, 1MHz FHSS
MAC Layer Review
  CSMA/CA (Ethernet Like) or RTS/CTS via “virtual carrier sense”
  BSS and ESS: roaming
  Authentication/Users Lists
Options
  Point Control Function
  Authentication via encrypted Shared Key (WEP)
Pictures from the Proxim website, 2002.

## Slide 7: 802.11b
Approved in 1999
2.4GHz
DSSS only w/ 20MHz channels
  Added 5.5 and 11Mbps data rates (CCK modulation)
  Backwards compatible with 802.11
No MAC changes

## Slide 8: 802.11a
Approved same time as 802.11b (Fall 1999)
A PHY layer extension only to the existing 802.11 standard- OFDM based waveform
  5GHz only, UNII bands 1,2 and 3
  Variable rates
    6,12,24Mbps mandatory
    9,18,36,48,54Mbps optional
  20MHz channels, 52 sub-carriers
MAC is unchanged
U-NII Bands
5GHz
6GHz
5.15-5.25GHz
5.25-5.35GHz
5.725-5.825GHz

## Slide 9: 802.11 e QoS
Under Development – many components of Whitecap
Enhanced support for QoS
  Adds a Hybrid Coordination Function – combination of PCF and DCF
  Enhanced DCF (EDCF)– 8 traffic categories, minimum of 4 physical queues
  Prioritization
  Optional MAC level FEC
  Jitter and Latency are adjustable parameters as well as min/max data rates
Goal – ability to handle voice and streaming media
 | Bandwidth | Latency | Jitter | Packet Loss
E-Mail | Low to moderate | High | high | Moderate
File Transfer (FTP) | Bursty high | high | high | low
ERP Applications | Moderate | moderate | high | Moderate
Web access (HTTP) | Bursty high | moderate | high | moderate
Video-conferencing | Sustained high | low | low | moderate
Voice over IP | Sustained low to moderate | low | low | moderate
Streaming media | Sustained moderate to high | moderate | Moder-ate | moderate

## Slide 10: 802.11i
IEEE has underway a task group called 802.1X – enhanced security for all Ethernet networks
802.11i is the wireless specific extension of 802.1x
Current WEP is 40bits with static keys
802.11i proposed 128 bit encryption
    Dynamic session keys
    Enhanced authentication

## Slide 11: 802.11g
Still in draft form, but largely complete
Purpose
  bringing higher data rates, a’ la 802.11a solutions, to the 2.4GHz band – up to 54Mbps
  Backwards compatible with 802.11b, something 802.11a is not.
Incorporates both OFDM and CCK over DSSS
Evolution of IEEE 2.4GHz WLAN Data Rates
Data Rate
(Mbps)
1
2
5
11
54
802.11
802.11b
802.11g

## Slide 12: 802.11h
Purpose – allay technical issues ETSI has with 802.11a to promote its acceptance in Europe
Key Features
  Transmit Power Control
  Dynamic Frequency Selection

## Slide 13: HiperLAN 2 A European Telecommunications Standards Institute- Broadband Radio Area Networks Standard for WLANs (ETSI BRAN)

## Slide 14: HiperLAN 2 and 802.11a Spectrum Comparison
5.1GHz
U-NII – 300MHz
5.200
5.400
5.600
5.8GHz
5.300
5.500
5.700
HiperLAN – 455MHz
5.15 - 5.25; 5.25 - 5.35
5.725 - 5.825
5.15 - 5.30
5.470 - 5.725

## Slide 15: HiperLAN 2 vs 802.11a
PHY layer almost the same
HiperLAN has TPC and DFS
HiperLAN supports selective ARQ
MAC QoS or Scheduler ready
56 and 168 bit DES encryption
Modulation | FEC | Data Rate-Mbps | HL2 | 11a
BPSK | ½ | 6 | X | X
BPSK | ¾ | 9 | X | X
QPSK | ½ | 12 | X | X
QPSK | 34 | 18 | X | X
16QAM | 1/2 | 24 |  | X
16QAM | 9/16 | 27 | X | 
16QAM | ¾ | 36 | X | X
64QAM | 2/3 | 48 |  | X
64QAM | 3/4 | 54 | X | X

## Slide 16: Home RF
Founded in March 1998
50 member companies (Intel, Motorola, Compaq…)
PHY Layer
  2.4GHz
  FHSS
  0.8Mbps,1.6Mbps, 5Mbps and 10Mbps
  1MHz and 5MHz channels
MAC Layer
  3 modes
    CSMA/CA
    Priority CSMA
    TDMA
  Support for both IP data and DECT telephony
  Roaming
Enhanced security -128 bit encryption

## Slide 17: Wireless Fidelity (WiFi)
Founded by the Wireless Ethernet Communications Alliance to promote interoperability and testing of 802.11 devices beyond the 802.11 standard.
Member companies such as 3COM, Cisco, Compaq etc.
All WiFi products are 802.11 All 802.11 products are not necessarily WiFi.

## Slide 18: Future applications
Home video distribution
  One box streams video to multiple monitors
Connect your Stereo to the Internet
Download MP3’s to your car
Appliances

## Slide 19: Conclusion
WLANs have a bright future in
  Hot Spots
  Enterprise
  Home
IEEE and HomeRF leading the way
With higher data rates, QoS, and better security applications are un-limited

## Slide 20
Thank You
David A. Sumi
Dsumi@telnecity.com
408 293-8158